## Slide 1: sra.c library

## Slide 2: Port Initialize
port_init();
Initializes the various ports as input and output.
PORT A, PORT B, PORT D are initialized as input ports while PORT C is initialized as output

## Slide 3: Delay Functions
delay_sec(int x);
Gives a time delay of ‘x’ seconds.
delay_milisec(int x);
Gives a time delay of ‘x’ miliseconds.
delay_microsec(int x);
Gives a time delay of ‘x’ microseconds.

## Slide 4: ADC Functions
adc_init();
Initializes the ADC mechanism of the microcontroller
Needs to be called in the main() for using the ADC feature
adc_start(unsigned char channel);
Returns the ADC value on the pin number passed in the argument.
‘channel’ is the pin number of PORT A

## Slide 5: PWM Functions
pwm1_init();
Initializes the pwm1 feature of the microcontroller
set_pwm1a(int a);
Sets the pwm1a value to ‘a’
set_pwm1b(int b)
Sets the pwm1b value to ‘b’

## Slide 6: Flick
flick ();
Flick is a function used to blink the LEDs.
LED needs to be initialized before using this function
Mainly used for debugging and a visual signal on completion of a task.

## Slide 7: LCD Functions
lcd_init(style);
Initializes the LCD pins. Needs to be called in the main() before using the LCD
‘style’ can be ‘blink’ or ‘underline’ depending upon the cursor you want
lcd_write_string(“string”);
Used to write a string of characters on the LCD starting from (0,0).

## Slide 8
lcd_write_string_xy(int x,int y,”string”);
Used to write a string starting from (x,y)
lcd_write_int_xy(int x,int y,int number,int fl)
Used to write a number at (x,y) with a field length fl.
lcd_clear();
Clears the LCD.

## Slide 9: USART Functions
usart_init();
Used to initialize the USART feature of the microcontroller
usart_transmit_char( unsigned char data );
Used to transmit a single character data
usart_transmit_string(“string”);
Used to transmit a string of characters

## Slide 10
usart_transmit_newline();
Used to transmit a newline
Transmit string and newline are used while interfacing with a PC
usart_receive_char();
Used to receive a single character
Returns the character received.

## Slide 11: Robot Motion Functions
bot_motion_init();
Initializes the motions. Needs to be called to make the bot move.
bot_left();
bot_left_backward();
bot_right();
bot_right_backward();

## Slide 12
bot_forward();
bot_backward();
bot_spot_left();
bot_spot_right();
bot_stop();
bot_brake();

## Slide 13: Switch Functions
switch_init();
Initializes the switches. Needs to be calle to use the switches
pressed_switch0();
pressed_switch1();
pressed_switch2();
pressed_switch3();
These functions return 1 or 0 if the switch is pressed or not.

## Slide 14: Line Following Functions
calibrate_black();
Calibrates the sensor values for a black surface
calibrate_white();
Calibrates the sensor values for a white surface

## Slide 15
set_threshold()
Sets a threshold value of the sensors
check_sensors()
Checks the sensors if they are 0 or 1 and modifies the variable sensorbyte accordingly