## Slide 1: USART

## Slide 2
AVR also has a dedicated hardware for serial communication this part is called the USART
USART - Universal Synchronous Asynchronous Receiver Transmitter

## Slide 3: Why USART
Serial communication occurs at standard speeds of 9600,19200 bps etc and this speeds are slow compared to the AVR CPUs speed.
The advantage of hardware USART is that you just need to write the data to one of the registers of USART and your done, you are free to do other things while USART is transmitting the byte.

## Slide 4: USART Registers
UDR - USART Data Register :
UCSRA - USART Control Status Registers
UCSRB
UCSRC
UBRRH and UBRRH : USART Baud rate register. But as we are using C language it is directly available as UBRR and compiler manages the 16BIT access.

## Slide 5
void usart_init(void)
{
UCSRC = (URSEL) | 0x06;
UBRRL = 0x67; //set baud rate lo
UBRRH = 0x00; //set baud rate hi
UCSRB = 0x98;
}

## Slide 6: BAUD rate
UBRR = - 1
Calculate the BAUD Rate and assign it to UBRR